## Slide 1
Stresses in Spur Gears
(AGMA Standards)
Dr. José Viriato Coelho Vargas
April 14, 2026
Department of Mechanical and Aerospace Engineering - MAE
EML3018C Mechanical Systems II

## Slide 2
Topics
American Gear Manufacturers Association (AGMA)
Practical applications of spur gears
Gear tooth nomenclature review
Stresses in spur gears
Bending Stresses – Ex. 12-5: Bending Stress Analysis (Norton, 2020)
Surface Stresses – Ex. 12-6: Surface Stress Analysis (Norton, 2020)
Gear materials – Ex. 12-7: Material Selection and Safety Factors (Norton, 2020)
Summary of the design strategy and more complex analyses overview

## Slide 3
1. AGMA
Definition: The American Gear Manufacturers Association (AGMA) is the primary body that supports research in gear design, materials, and manufacturing.
Role: AGMA publishes the standards for the design, manufacture, and assembly of gears, ensuring they are highly standardized regarding tooth shape and size.
Standardization: Because of AGMA, designers can use simplified approaches (like the one presented here) or more complex methods found in specialized AGMA publications to ensure gear reliability.

## Slide 4
2. Practical Applications of Spur Gears
Spur gears are used to transmit torque and angular velocity between parallel shafts. Examples:
Automobile Transmissions: A common application where gearsets exchange torque for velocity to drive heavy loads.
Rack-and-Pinion Steering: Converts the rotary motion of the steering wheel into the linear translation of a rack to steer the car's wheels.
Aircraft Servomechanisms: Used in critical control surfaces.

## Slide 5
3. Gear tooth nomenclature review

## Slide 6
4. Stresses in spur gears (two modes of failure)

## Slide 7
4. Stresses in spur gears (Design)

## Slide 8
5. Bending Stresses
THE LEWIS EQUATION: the tooth is a cantilever beam with its critical section at the root. From the bending stress equation in a cantilever beam, he derived in 1892 the following equation:
THE BENDING STRESS EQUATION: valid only for certain assumptions about tooth and gear-mesh geometry (e.g., contact ratio between 1 and 2) – motivation for more complex analyses. J and K’s are empirical terms.

## Slide 9
5. Bending Stresses
Example 12-5
Bending Stress Analysis of a Spur-Gear Train
This example analyzes a three-gear train (pinion, idler, and gear) with a transmitted load Wt = 432 lb.
Initially, estimate the face width:

## Slide 10
5. Bending Stresses

## Slide 11
6. Surface Stresses
The stresses at the tooth surface are dynamic Hertzian contact stresses in combined rolling and sliding. Buckingham equation for surface stresses in gear teeth:
Surface geometry factor I in Eq. (12.22) takes into account the radii of curvature of the gear teeth and the pressure angle in empirical formulae.
The surface finish factor Cf considers rough surface finishes on teeth – usually 1.
The elastic coefficient Cp (psi0.5 or MPa0.5) considers different tooth materials:

## Slide 12
6. Surface Stresses
Example 12-6
Surface Stress Analysis of a Spur-Gear Train
This analysis uses the same gear train to determine the contact (Hertzian) stresses between mating teeth.

## Slide 13
7. Gear materials
A limited number of metals and alloys are suitable for gears that transmit significant power (Table 12-18) – Steels, cast irons, and malleable and nodular irons – most common choices for gears.
Bending-fatigue strengths and Surface-fatigue strengths need to be accessed for the analysis. AGMA states for 107 cycles of repeated stress for 99% reliability level. So, correction is needed for other conditions different from AGMA tests.

## Slide 14
7. Gear materials

## Slide 15
7. Gear materials

## Slide 16
7. Gear materials
AGMA bending-fatigue (steels) and surface-fatigue strengths (through-hardened steels)

## Slide 17
7. Gear materials
Example 12-7
Material Selection and Safety Factors for Spur Gears
Select suitable materials and calculate the safety factors for both bending and surface stresses in the 3-gear train.
Service life is 5 years of one-shift operation. All gears are steel. T = 200oF.
• Initial Selection: Using AGMA Grade 2 steel (through-hardened to 250 HB).
• Corrected Strengths:
o Bending Fatigue Strength (Sfb): 38,937 psi.
o Surface Fatigue Strength (Sfc): 105,063 psi.

## Slide 18
7. Gear materials

## Slide 19
7. Gear materials
Small design change will improve these. Increase face width from 2.0 to 2.5 in (15 / pd) – reduces all stresses and gives new safety factors

## Slide 20
8. Summary of the design strategy
• Two Failure Modes: Gears must be checked for both bending fatigue (fracture at the root) and surface fatigue (pitting).
• Catastrophic vs. Gradual: Bending failure is sudden and catastrophic, disabling the machine immediately. Surface failure is gradual, often providing audible or visible warnings before total failure.
• Strategy: Safety factors for bending (Nb) should generally be higher than those for surface failure (Nc). This ensures that if the gear does fail, it fails via the more "desirable" (non-catastrophic) pitting mode rather than tooth breakage.
• Iteration: adjust face width and materials hardness to meet surface life requirements. Ensure surface failure happens long before a tooth breaks.

## Slide 21
8. More complex analyses overview
Thermal and structural analysis of spur gears with the Finite Element Method (FEM)

## Slide 22
Acknowledgements
Dr. José V. C. Vargas
CONTACT
vargasjvcv3@gmail.com
@Jose Viriato Coelho Vargas
http://servidor.demec.ufpr.br/laboratorios/lft/gect/
https://www.adscientificindex.com/subject-rankings/?q=jose+viriato+coelho+vargas
Thank you!

## Slide 23
References
Robert L. Norton, Machine Design: An Integrated Approach, 6th edition, Pearson, 2020, ISBN: 9780135184233
Richard Budynas and Keith Nisbett, Shigley's Mechanical Engineering Design, 11th edition, McGraw Hill, 2019, ISBN: 9780073398211