## Slide 1: Rocketry Trajectory Basics
LabRat Scientific
© 2018

## Slide 2
Difference Between Orbital and Sub-Orbital Trajectories
A sub-orbital trajectory is a flight path that impacts the earth
A sub-orbital trajectory is sometimes referred to as an “earth intersecting orbit”. If we shrunk the earth to a point mass, the rocket would actually orbit around that point.
A sub-orbital rocket can reach altitudes higher than low earth orbiting satellites, but the rocket can’t generate the required velocity to achieve orbit.

## Slide 3
Difference Between Orbital and Sub-Orbital Trajectories
Sub-orbital rockets are generally launched at launch angles as low as ~ 75 degrees (from the horizontal), but are usually launched at angles around 82 degrees.
Orbital rockets go through a pitch maneuver, so much of the velocity is applied in the horizontal direction.
If a sounding rocket was pitched over after launch like an orbital rocket, the maximum velocity would only be on the order of 8,000 MPH.

## Slide 4: General Shape of a Suborbital Trajectory
No Atmosphere
NASA Sounding Rocket
Model Rocket
Atmosphere
“Boundary” of space
(~ 100 km)

## Slide 5
No Atmosphere
A model rocket stays in the atmosphere and is always under the influence of drag. The drag decreases the horizontal velocity (as well as the vertical velocity) and the flight path becomes “squished”
Atmosphere
A NASA Sounding Rocket is outside the atmosphere for most of the flight, so the flight path is nearly parabolic.
General Shape of a Suborbital Trajectory
“Boundary” of space
(~ 100 km)

## Slide 6: General Rocket Velocity
The rocket begins to move when the thrust force becomes greater than the weight of the rocket

## Slide 7
The thrust force causes the rocket to accelerate and the velocity increases over time…
General Rocket Velocity

## Slide 8
Maximum velocity is achieved just before rocket motor burn out…
General Rocket Velocity

## Slide 9
Burn out
General Rocket Velocity

## Slide 10
After burnout, only gravity and drag are acting on the rocket. Both are trying to slow down the rocket…
General Rocket Velocity

## Slide 11
The rocket slows down as it reaches apogee.
General Rocket Velocity

## Slide 12
Apogee is the highest point in the flight. It is also the point where the rocket is flying the slowest…
General Rocket Velocity

## Slide 13
On the down leg, gravity acts to accelerate the rocket so the speed begins to increase.
General Rocket Velocity

## Slide 14
The velocity continues to increase as the rocket freefalls towards the ground.
General Rocket Velocity

## Slide 15
However, drag is still acting on the rocket, and that drag retards the acceleration…
General Rocket Velocity

## Slide 16
At some point, the drag force will equal the weight of the rocket and acceleration will become zero.
General Rocket Velocity

## Slide 17
This condition is known as “terminal velocity”.
General Rocket Velocity

## Slide 18
Body Attitude vs. Velocity Vector
The Body Attitude is the angle between the local horizontal and the “long axis” of the rocket.
The Velocity Vector is a line that represents the direction the rocket is actually moving. It is also referenced to the local horizontal.
Local Horizontal

## Slide 19: Flight Path Angle
The Flight Path Angle is the angle between the velocity vector and the local horizontal.
The flight path angle can be referenced from the vertical or the horizontal. This lesson references the flight path angle to the local horizontal.

## Slide 20
The term “local horizontal” is used, because if the flight covers a significant distance, the curvature of the earth causes the “horizontal” to change. Horizontal means “parallel to the earth’s surface”.
Flight Path Angle
Local Horizontal

## Slide 21
Flight Path Angle is positive on the upleg
Flight Path Angle

## Slide 22
Flight Path Angle is negative on the downleg
Flight Path Angle

## Slide 23
Model Rocket - Flight Path Angle and Body Angle
The longitudinal (long) axis of the rocket will always be parallel to the velocity vector of the rocket.

## Slide 24
Model Rocket - Flight Path Angle and Body Angle
The longitudinal (long) axis of the rocket will always be parallel to the velocity vector of the rocket.

## Slide 25
Model Rocket - Flight Path Angle and Body Angle
The longitudinal (long) axis of the rocket will always be parallel to the velocity vector of the rocket.

## Slide 26
Model Rocket - Flight Path Angle and Body Angle
The longitudinal (long) axis of the rocket will always be parallel to the velocity vector of the rocket.

## Slide 27
Model Rocket - Flight Path Angle and Body Angle
The longitudinal (long) axis of the rocket will always be parallel to the velocity vector of the rocket.

## Slide 28
Model Rocket - Flight Path Angle and Body Angle
The longitudinal (long) axis of the rocket will always be parallel to the velocity vector of the rocket.

## Slide 29
Model Rocket - Flight Path Angle and Body Angle
The longitudinal (long) axis of the rocket will always be parallel to the velocity vector of the rocket.

## Slide 30
Model Rocket - Flight Path Angle and Body Angle
The longitudinal (long) axis of the rocket will always be parallel to the velocity vector of the rocket.

## Slide 31
Model Rocket - Flight Path Angle and Body Angle
The longitudinal (long) axis of the rocket will always be parallel to the velocity vector of the rocket.

## Slide 32
Sounding Rocket - Flight Path Angle and Body Angle
“Boundary” of space
(~ 100 km)

## Slide 33: Sounding Rocket - Flight Path Angle and Body Angle
“Boundary” of space
(~ 100 km)

## Slide 34
Sounding Rocket - Flight Path Angle and Body Angle
“Boundary” of space
(~ 100 km)
Once the sounding rocket leaves the atmosphere, there is no aerodynamic moment generated by the fins, thus the rocket will not pitch over…

## Slide 35
Sounding Rocket - Flight Path Angle and Body Angle
“Boundary” of space
(~ 100 km)
Once the sounding rocket leaves the atmosphere, there is no aerodynamic moment generated by the fins, thus the rocket will not pitch over…

## Slide 36
Sounding Rocket - Flight Path Angle and Body Angle
“Boundary” of space
(~ 100 km)
Once the sounding rocket leaves the atmosphere, there is no aerodynamic moment generated by the fins, thus the rocket will not pitch over…

## Slide 37
Sounding Rocket - Flight Path Angle and Body Angle
“Boundary” of space
(~ 100 km)
Once the sounding rocket leaves the atmosphere, there is no aerodynamic moment generated by the fins, thus the rocket will not pitch over…

## Slide 38
Sounding Rocket - Flight Path Angle and Body Angle
“Boundary” of space
(~ 100 km)
Once the sounding rocket leaves the atmosphere, there is no aerodynamic moment generated by the fins, thus the rocket will not pitch over…

## Slide 39
Sounding Rocket - Flight Path Angle and Body Angle
“Boundary” of space
(~ 100 km)
Once the sounding rocket leaves the atmosphere, there is no aerodynamic moment generated by the fins, thus the rocket will not pitch over…

## Slide 40
Sounding Rocket - Flight Path Angle and Body Angle
“Boundary” of space
(~ 100 km)
Once the sounding rocket leaves the atmosphere, there is no aerodynamic moment generated by the fins, thus the rocket will not pitch over…

## Slide 41
Sounding Rocket - Flight Path Angle and Body Angle
“Boundary” of space
(~ 100 km)
Once the sounding rocket leaves the atmosphere, there is no aerodynamic moment generated by the fins, thus the rocket will not pitch over…

## Slide 42
Sounding Rocket - Flight Path Angle and Body Angle
“Boundary” of space
(~ 100 km)
When the sounding rocket reenters the atmosphere, the fins will cause the rocket to align with the velocity vector once again.

## Slide 43
Sounding Rocket - Flight Path Angle and Body Angle
“Boundary” of space
(~ 100 km)
When the sounding rocket reenters the atmosphere, the fins will cause the rocket to align with the velocity vector once again.

## Slide 44
Sounding Rocket - Flight Path Angle and Body Angle
“Boundary” of space
(~ 100 km)
When the sounding rocket reenters the atmosphere, the fins will cause the rocket to align with the velocity vector once again.

## Slide 45
Sounding Rocket Factoid
During ascent, the payload is attached to the upper stage rocket motor. This figure shows the third stage of a three-stage sounding rocket
Once in space, the payload separates from the rocket motor so it can then do the things necessary to collect the scientific data (pointed towards a deep space object, deploy sensor booms, or eject sub-payloads). The motor will realign with the velocity vector during reentry, but the payload will generally tumble because it doesn’t have fins and is neutrally stable…

## Slide 46
This is a plot of a trajectory simulation for a two-stage NASA Sounding rocket known as a “Terrier Malemute”.
Notice how the trajectory is parabolic.
Sounding Rocket – Altitude vs. Time plot

## Slide 47: Sounding Rocket – Velocity and Acceleration, Staging
0
10
20
30
40
50
60
70
80
90
100
110
0
500
1000
1500
2000
2500
3000
3500
4000
Time - Sec
Velocity vs Time
Velocity - mps
0
10
20
30
40
50
60
70
80
90
100
110
-5
0
5
10
15
20
Time - Sec
Acceleration vs Time
Acceleration - Gs
This is the velocity prediction for a 4-stage sounding rocket.
This is the acceleration trace for the same rocket. Notice that the first and second stage motors have very short burn times. These motors are known as “boosters”. The longer burning upper stage motors are known as “sustainers”. Booster motors get the rocket moving quickly so aerodynamic stability can be achieved.
The vehicle accelerates during motor burn, then decelerates during coasting phase due to drag and gravity. The rocket coasts between motor burns in order to reduce bending loads.

## Slide 48: Calculating Rocket Acceleration
Force = Mass x Acceleration
Forces at Play: Thrust
Gravity (weight)
Drag
(Thrust - Drag - ( Weight x Sin (Flt Path) )
Acceleration = --------------------------------------------------------------------
Mass
Thrust (if it exists) is always positive
Drag is always negative
The effect of “weight” depends on whether the rocket is moving upwards or downwards
Force
Acceleration = ------------
Mass

## Slide 49
Force = Mass x Acceleration
(Thrust - Drag - ( Weight x Sin (Flt Path) )
Acceleration = --------------------------------------------------------------------
Mass
Thrust (if it exists) is always positive
Drag is always negative
The effect of “weight” depends on whether the rocket is moving upwards or downwards
Force
Acceleration = ------------
Mass
Forces at Play: Thrust
Gravity (weight)
Drag
Calculating Rocket Acceleration

## Slide 50
Force = Mass x Acceleration
(Thrust - Drag - ( Weight x Sin (Flt Path) )
Acceleration = --------------------------------------------------------------------
Mass
Thrust (if it exists) is always positive
Drag is always negative
The effect of “weight” depends on whether the rocket is moving upwards or downwards
Force
Acceleration = -----------
Mass
Forces at Play: Thrust
Gravity (weight)
Drag
Calculating Rocket Acceleration

## Slide 51
Force = Mass x Acceleration
(Thrust - Drag - ( Weight x Sin (Flt Path) )
Acceleration = --------------------------------------------------------------------
Mass
Thrust (if it exists) is always positive
Drag is always negative
The effect of “weight” depends on whether the rocket is moving upwards or downwards
Force
Acceleration = -----------
Mass
Forces at Play: Thrust
Gravity (weight)
Drag
Calculating Rocket Acceleration

## Slide 52
Force = Mass x Acceleration
(Thrust - Drag - ( Weight x Sin (Flt Path) )
Acceleration = --------------------------------------------------------------------
Mass
Thrust (if it exists) is always positive
Drag is always negative
The effect of “weight” depends on whether the rocket is moving upwards or downwards
Force
Acceleration = -----------
Mass
Forces at Play: Thrust
Gravity (weight)
Drag
Calculating Rocket Acceleration

## Slide 53: Drag
Drag = ½ x Air Density x Velocity 2 x Cd x Ref Area
The drag acting on the rocket is a function of its shape and size, as well as the air density, and velocity…
As the rocket speeds up, the drag acting on it increases.

## Slide 54: Terminal Velocity
( Thrust - Drag - ( Weight x Sin (Flt Path) )
Acceleration = --------------------------------------------------------------------
Mass
( - Drag - ( - Weight ))
Acceleration = -----------------------------------
Mass
( - Drag + Weight )
Acceleration = ------------------------------------
Mass

## Slide 55: Terminal Velocity
( Thrust - Drag - ( Weight x Sin (Flt Path) )
Acceleration = --------------------------------------------------------------------
Mass
( - Drag - ( - Weight ))
Acceleration = -----------------------------------
Mass
( - Drag + Weight )
Acceleration = ------------------------------------
Mass
This analysis assumes the rocket is coasting so thrust is zero.

## Slide 56: Terminal Velocity
( Thrust - Drag - ( Weight x Sin (Flt Path) )
Acceleration = --------------------------------------------------------------------
Mass
( - Drag - ( - Weight ))
Acceleration = -----------------------------------
Mass
( - Drag + Weight )
Acceleration = ------------------------------------
Mass
We will assume the rocket is falling straight down towards the earth. Sine (-90) = - 1.0

## Slide 57: Terminal Velocity
( Thrust - Drag - ( Weight x Sin (Flt Path) )
Acceleration = --------------------------------------------------------------------
Mass
( - Drag - ( - Weight ))
Acceleration = -----------------------------------
Mass
( - Drag + Weight )
Acceleration = ------------------------------------
Mass
A negative times a negative is a positive.

## Slide 58: Terminal Velocity
( Thrust - Drag - ( Weight x Sin (Flt Path) )
Acceleration = --------------------------------------------------------------------
Mass
( - Drag - ( - Weight ))
Acceleration = -----------------------------------
Mass
( - Drag + Weight )
Acceleration = ------------------------------------
Mass
When Drag is equal to Weight, the numerator becomes zero.
When the numerator is zero, the acceleration is zero.

## Slide 59: Terminal Velocity
( - 5 lbs + 5 lbs )
Acceleration = ------------------------------------
Mass
Drag is always negative. In this application, weight is positive when the object is falling downwards.
When the numerator is zero, the acceleration is zero.
0
Acceleration = ----------------------------------
Mass
Acceleration = 0
Zero acceleration means the rocket is neither speeding up nor slowing down. This is known as Terminal Velocity…

## Slide 60
Drag = ½ x Air Density x Velocity 2 x Cd x Ref Area
Terminal Velocity: Drag = Weight
Air Density: 0.00237 (lb*sec2) / ft4
Rocket Cd: 0.41
Ref Area: 0.049 Ft2
Weight: 1.4 lbs (= Drag for Terminal Velocity)
2 * Drag
Velocity = ----------------------------------------
Air Density x Cd x Ref Area
Velocity = 242 ft/sec
Model Rocket Terminal Velocity Sample Calculation
The key point is the fact that the drag will equal the rocket’s weight when terminal velocity is achieved. We can use the drag equation to backout the velocity required to generate the needed drag…

## Slide 61: Rocket Staging
Flying high, or achieving orbit, requires the rocket to reach a high velocity…
Achieving a high velocity require the rocket to have a high acceleration…
Newton’s Second Law indicates acceleration is inversely proportional to mass…
So, if we reduce mass, then acceleration will be higher…
The consumption of fuel reduces mass – that helps…
But what about the empty motor casings or fuel tanks? At some point, the rocket is just carrying dead weight…
Dropping off stages, reduces unneeded weight, and thus, increases acceleration.
F
a = -------
M

## Slide 62: Questions?